## Slide 1: Everton unconstrained smooth model

## Slide 2: Introduction
Josh Phillips (JP geoscience) requested a quick unconstrained smooth model inversion of a weak (~35nT) magnetic anomaly near Everton.
The following is a brief outline of the model results. I only spent 1 day on this to minimise project costs
The anomaly is a rough semicircle superimposed on a broader, much deeper, magnetic source
The existing magnetic data is the 2007 NE Tas helimagnetic survey, on 200m E-W lines (shown to the right)
The width and character of the anomaly suggest the source is not as close to surface as some of the other anomalies that Josh selected
There is almost certainly remanence, however it is not immediately apparent visually
I clipped the magnetic data to the area surrounding the anomaly
The inversion used the mginv3D algorithm developed by John Paine (Scicomapp Pty Ltd), which is based on the UBC approach to inverse modelling
It is important to be aware that the potential field interpretation has an intrinsic limitation due to its no uniqueness; as a consequence, determination of actual structure below of these anomalies will require more constraints on depths and magnetisation than those presently available.
  In otherwords, unconstrained smooth models are exceedingly unreliable!
5nT contours, TMI and flight path

## Slide 3: ……continued
The model mesh is 40x40x20m, compression using Daubechies Wavelet 4, with moderate depth weighting (beta 3, znot 100)
Terrain model is the 5m GA elevation model
TMI inversion used the point data (not gridded TMI) and true terrain offset (radar alt). This produces a better fit in areas with strong topography.
The VRMI (vector residual magnetic intensity) inversion used the VRMI transformed TMI grid with a vertical inducing field and 70m constant terrain offset, and no high pass filter.
Why/what is VRMI?
  Short answer: A rather non-scientific approach to minimising effect of remanent magnetisation.
  Any model assuming no remanence (i.e. TMI only) will put any remanent magnetised bodies the wrong location and give them the wrong geometry.
  The ‘wrongness’ of the resultant TMI can range from not noticeable, to completely and utterly wrong
  The degree and direction of wrongness strength and direction of the remanence, body geometry, size, depth, and location. In most cases, it is impossible to see whether remanence is significant just by ‘looking at the data’
  Mark Dransfield and John Paine noticed that the total gradient of the TMI is less dependant on the direction of magnetisation (i.e. remanence). i.e. there is thus a much stronger spatial correlation between the highs in these transformed responses for strongly remanent magnetised bodies than there is in the original TMI and RTP data, so inversions using such data can potentially be useful in generating insight into the geometry of the magnetic sources.
  There is, however, a distinct lack of theoretical rigour. The VRMI is the magnitude A of the anomalous magnetic field response B, that is A = sqrt(Bx2+By2+Bz2). In other words, it is the ‘total gradient’ of the magnetic field. It is a ‘gradient’ signal (units nT/m), not an absolute signal……yet we pretend it is proper magnetics and do a model on it.
VRMI tends to overestimate depth and width.
Also, the VRMI filtering process attenuates the low frequency content; as a consequence, the total magnetisation is overall reduced, and any deep sources are lost.
Moreover, the inversion technique we adopted generates smooth models that smear the sources and hence lower the peak susceptibilities.
5nT contours, TMI and flight path
Dransfield M. Christensen A. Liu G. 2003 Airborne vector magnetics mapping of remanently magnetized banded iron formations at Rocklea, Western Australia Explor. Geophys. 34 9396

## Slide 4: Everton_VRMI_coarse.msh&sus
Most of this misfit is related to two unavoidable sources:
The VRMI is not a true magnetic field and does not quite have a proper shape. This means the model can not fit edges or very short wavelength anomalies very well.
There are gridding artefacts intrude by the TMI gridding, and then again by the VRMI algorithm
When we model VRMI we are forced to use a constant terrain offset so helicopter elevation is incorrect

## Slide 5: Everton_TMI_coarse.msh&sus
Unlike VRMI, TMI can be done on the actual magnetic readings and thus can use the radar altimeter level for each point (rather than assuming a constant 70m above surface). This minimises errors introduced into the model due to incorrect height.
However we can not really say if this is a better model than the VRMI because there are still strong misfits. In this case, the misfits are typical of remanence.
Note that gaps are due modelling algorithm not being a very clever gridding algorithm, it is not related to no data

## Slide 6: Comparison between the TMI and VRMI
TMI shows a weak (~35nT) ring-like feature superimposed on a deeper magnetic unit
In TMI, the deeper magnetic features are those with long wavelengths, smoother, and gentle gradients
VRMI – because it is a gradient filter - gets rid of the long/low gradient (deeper magnetic units)
It highlights the shallower things but also make them too broad. This causes higher misfit around the edges of sources
There appears to be a edge-effects related problem with VRMI on the west because the grid was clipped too small before the VRMI was calculated. This anomaly should be ignored.

## Slide 7: 3D Magnetic inversion voxel models
In the left figure, TMI model is in red and VRMI model is in yellow. VRMI filter is a gradient filter and thus the deeper (smooth, low gradient) fields are removed. This explains why the is no deep material in the VRMI model also explains why VRMI model does not show a deep core whereas the TMI model does. In this case, the TMI model is more correct for the deeper sources.
The right figure shows the TMI model >0.0008 SI as a yellow isosurface. The VRMI, also clipped to >0.0008 SI, is shown in pink. I have clipped the bottom part of the TMI model at 127mRL to better show the contrast between the two models. Generally, the TMI makes the source a fair bit shallower than the VRMI. However, these two models overlap pretty much close to one another except from depth to top.

## Slide 8: How close are the two models?
TMI and VRMI models sliced at ~350m above sea level. There is a distinct offset between the two models, probably related to remanence. Any drilling show try to test the strongest parts of both models

## Slide 9: TMI and VRMI models sliced at ~250m above sea level. This anomaly is stronger near surface and thus more apparent in the 350mRL slice.

## Slide 10: Parts of the model to avoid
Most parts of inversion models are not trustworthy and it is very important to be mindful of a few below mentioned points:
The edges of the model are completely unreliable
Never trust the lower edges of anomalies – the regional removal process means that the bottom parts of anomalies are ‘clipped off’
This apparent magnetic layer and non-magnetic basement are an artefact of the regional removal and should not be targeted for drilling